## Slide 1: Hyperspectral Data Classification
Jun Chen, Dan Wang,
Zhou Zhang, Penghao Wang

## Slide 2: Hyperspectral Image: Indian Pine
Indian Pine Agriculture, Indiana
AVIRIS airborne, June 1992
220 spectral bands
Spectral resolution 10nm
Spatial resolution 20m
16 classes of crops
RGB Image
Ground Reference

## Slide 3: Supervised Classifiers
Considering the high dimensionality of the data, we used the following three classifiers:
  Kernel SVM
    Gaussian kernel, cross-validation for parameter selection
  Random Forest
    Number of trees and number of features that were tested in each split were tested via cross validation
  Adaboost
    Decision tree, cross-validation

## Slide 4: Data Preprocessing
Remove noisy spectral bands (features), and use 200 out of 220 as final features.
Ignore minor classes with very labeled samples, and focus on 12 out of 16 classes.
For each class, randomly select 100 labeled samples for training and 100 for testing.
Normalize the data for each feature.

## Slide 5: Results Evaluation (Testing Accuracy)
 | Kernel SVM | Random Forest | Adaboost
Overall Accuracy | 0.85 | 0.80 | 0.82
Corn-no till (C1) | 0.72 | 0.68 | 0.71
Corn-min till (C2) | 0.67 | 0.60 | 0.55
Corn (C3) | 0.91 | 0.84 | 0.88
Soybeans-no till (C4) | 0.82 | 0.77 | 0.76
Soybeans-min till (C5) | 0.77 | 0.77 | 0.80
Soybeans-clean till (C6) | 0.78 | 0.66 | 0.70
Grass/Pasture (C7) | 0.95 | 0.91 | 0.95
Grass/Trees (C8) | 0.94 | 0.91 | 0.94
Hay-windrowed (C9) | 0.99 | 0.99 | 0.99
Wheat (C10) | 0.99 | 0.99 | 0.99
Woods (C11) | 0.83 | 0.84 | 0.82
Building-Grass-Trees-Drive (C12) | 0.78 | 0.65 | 0.78